## Slide 1
28th Congress of SCTM, 23-26 September, Ohrid, Macedonia
DEVELOPMENT AND OPTIMIZATION OF AN HPLC-UV-DAD METHOD FOR SIMULTANEOUS QUANTIFICATION OF CEFIXIME AND SODIUM BENZOTE IN ORAL SUSPENSION
Marijana Pejik1,2, Marina Stefova2, Stevce Petrovski1, Maja Gjorgjeska1, Sanja Kovacevska1, Magdalena Atanasovski1
e-mail: mpejic@alkaloid.com.mk
1 Alkaloid AD Skopje, Skopje, Macedonia
2 Institute of Chemistry, Faculty of Natural Sciences and Mathematics, Skopje, Macedonia
Antibiotics, especially cephalosporins, are widely used in modern medicine. Cefixime, a semisynthetic third-generation cephalosporin, is commonly formulated as an oral suspension containing sodium benzoate as a preservative. Current quantification procedures require separate analytical methods due to the different properties of the active ingredient and preservative. The aim of this study was development, optimization and validation of a simple, rapid, sensitive and specific HPLC method for simultaneous determination of cefixime and sodium benzoate in oral suspensions.
Introduction & Aim
Method development
Several HPLC and UHPLC columns were evaluated. While UHPLC provided faster analysis, HPLC showed better robustness for the oral suspension matrix. Mobile phase composition, flow rate, injection volume and detection wavelengths were optimized to achieve adequate separation and reliable quantification of sodium benzoate, cefixime and impurity D. The selected conditions provided good resolution and reproducible performance. (Table 1)
000
Table 1 Chromatographic parameters results (Vinj – injection volume, N – number of theoretical plates, As – asymmetry factor, R – resolution, tr – retention time)
Materials & methods
System | Nexera i Series
Column | Waters XBridge C18, 4.6 × 100 mm, 3.5 µm
Mobile phase | 77% TBAH buffer (31.6 mM, pH 6.5) / 23% ACN
Flow rate | 1.5 mL/min
Detection | 223 nm (Sodium benzoate) / 254 nm (Cefixime)
Temperature | 40 °C
Autosampler | 5 °C
Injection | 5 µL
Conclusion
The developed HPLC method is suitable for routine QC and regulatory applications. Simultaneous quantification of both analytes in a single run reduces analysis time, solvent consumption and laboratory costs.
Results & discussion
Fig. 1. Chromatogram at 223 nm from diluent, placebo, resolution, standard and sample solution
Fig. 2. Chromatogram at 254 nm from diluent, placebo, resolution, standard and sample solution
Method robustness was demonstrated through intentional variations in acetonitrile content, buffer pH, flow rate, column lot, and column temperature.
Specificity
Accuracy
Linearity
Precision
Robustness
Isocratic elution of both analytes achieved
in 12 minutes
Retention time of Cefixime: 7.8 minutes
Retention time of Sodium benzoate: 2.4 minutes
 | R2>0.999
Sodium benzoate | 1.000
Cefixime | 1.000
 | Sodium benzoate (98-102 %) | Cefixime (98-102 %)
80 % | 101.22 | 99.62
100 % | 99.35 | 99.53
120 % | 101.13 | 100.56
 | System precision (%) RSD< 2.0 | 
 | Ret. time | Area
Sodium benzoate | 0.2 | 0.6
Cefixime | 0.1 | 0.3
 | Method precision (%) RSD< 2.0 |  | 
 | Ret. Time | Area | Amount
Sodium benzoate | 0.2 | 0.3 | 0.4
Cefixime | 0.1 | 0.3 | 0.5