## Slide 1
28th Congress of SCTM, 23-26 September, Ohrid, Macedonia
Marijana Nikoloska1, Silvana Janevikj2, Katerina Kochova3, Irena Slaveska Spirevska4, Tanja Bakovska Stoimenova5, Elena Petrovska Kostadinoska6, Kristina Grncharoska7
1 Replek Farm Ltd, Skopje, North Macedonia, marijana.nikolovska@replek.mk, 2,3,4,5,6,7 Replek Farm Ltd, Skopje, North Macedonia
Risperidone (a)
Used solvent:
Methanol and 0.08% H3PO4
in a 7 : 3 (v/v) ratio
Experimental
The use of an acidified extraction medium ensures robust and reproducible recovery, while the optimized HPLC method provides accurate and reliable quantification suitable for routine cleaning validation in risperidone manufacturing.
Conclusions
Results and discussion
Reference substance:
Risperidone CRM
HPLC system and conditions:
analytical column: LiChrospher RP Select B 125 mm x 4.0 mm, 5 µm
mobile phase: 0.25% KH2PO4 buffer (pH 3.0) and Acetonitrile in a 66 : 34 (v/v) ratio
isocratic conditions;
flow rate: 1.0 mL/min.;
detection wavelength: 235 nm;
column temperature: 35° C;
injection volume: 50 µL
Swab recovery: acidified methanol achieved recovery >80% (acceptance criterion), while plain methanol gave lower recovery — confirming the acidified medium as the optimal swab solvent for risperidone cleaning validation.
The HPLC method was validated with respect to selectivity, linearity, precision, and sensitivity, with the limit of detection (LOD) and limit of quantification (LOQ) being determined.
OPTIMIZATION OF AN HPLC METHOD FOR RISPERIDONE
QUANTIFICATION FOR CLEANING VALIDATION PURPOSES
Introduction & Aim
Risperidone (a), chemically known as 3-[2-[4-(6-fluoro-1,2-benzoxazol-3-yl)piperidin-1-yl]ethyl]-2-methyl-6,7,8,9-tetrahydropyridol[1,2-a]pyrimidin-4-one, is indicated for the treatment of schizophrenia, bipolar disorder and related psychiatric conditions.
The aim of this study was to optimize the swabbing procedure and high performance liquid chromatography (HPLC) method conditions for risperidone cleaning validation.
000