## Slide 1
28th Congress of SCTM, 23-26 September, Ohrid, Macedonia
Zharko Tanturovski¹˒², Zhaklina Poposka Svirkova¹˒²*, Marija Andonovska¹˒³, Dragica Doneva¹, Zana Mustafa¹, Sanija Zulfikjari¹, Aleksandra Dimitrovska¹, Sandra Zinoski¹, Zorica Arsova Sarafinovska¹˒², Katerina Starkoska¹
¹ Institute for Public Health of the Republic of Macedonia, Skopje | ² Faculty of Medical Sciences, Goce Delcev University, Stip | ³ Faculty of Dentistry – Skopje, Ss. Cyril and Methodius University in Skopje
Electronic cigarettes require reliable quality control of e-liquids, particularly nicotine, whose declared concentration commonly ranges from 0–20 mg/mL. HPLC is widely used for nicotine determination because of its robustness and sensitivity. However, nicotine can show poor peak symmetry on conventional C18 phases because of interactions with residual silanol groups. AIM: To compare three stationary phases—end-capped C18, conventional C8 and phenyl-hexyl—for nicotine determination in commercial e-liquids, focusing on efficiency, peak symmetry, reproducibility and analytical sensitivity.
Introduction & Aim
Experimental
Conclusions
Results and discussion
The author acknowledges his own dedication and efforts in the completion of this study. 
Acknowledgement
AEC-P15
Columns evaluated
Column | Stationary phase | Dimensions
A | Purospher® Star RP18e (end-capped C18) | 250 × 4.6 mm, 5 µm
B | Hypersil BDS C8 | 250 × 4.6 mm, 5 µm
C | ZORBAX Eclipse Plus Phenyl-Hexyl | 250 × 4.6 mm, 5 µm
• End-capped C18 (Column A) showed the best overall performance. • Highest efficiency: NTP = 8409; best peak symmetry: tailing factor = 1.1. • Calibration linearity was excellent (r² = 0.9999); LOD = 0.0098 mg/mL; LOQ = 0.0298 mg/mL. • Commercial e-liquid contained 19.80 mg/mL nicotine (99% of the declared value). • The HPLC-DAD method is suitable for routine nicotine quality control.
1. Column performance comparison
Parameter | Column A: C18 | Column B: C8 | Column C: Phenyl-hexyl
Efficiency (NTP) | 8409 | Not reported | Intermediate
Peak symmetry / tailing | 1.1 (best) | ≈0.6 (fronting) | Intermediate
Overall assessment | Superior | Lower symmetry | Intermediate
2. Quantitative performance – optimal Column A
Metric | Result
Calibration range | 0.4242–1.2726 mg/mL
Linearity | r² = 0.9999
LOD / LOQ | 0.0098 / 0.0298 mg/mL
Repeatability (n = 6) | RT RSD 0.29%; peak area RSD 0.19%
3. Commercial e-liquid
19.80 mg/mL nicotine | 99% of declared 20 mg/mL
Purospher® Star RP18e
Hypersil BDS C8
Phenyl-Hexyl
Performance evaluation of different HPLC columns in analysis of nicotine from e-liquids