## Slide 1
28th Congress of SCTM, 23-26 September, Ohrid, Macedonia
SUSTAINABLE VALORIZATION OF ORANGE PEEL WASTE BY SUPERCRITICAL CO₂ EXTRACTION: GC–MS AND RAMAN SPECTROSCOPIC CHARACTERIZATION
Mina Volić Ollier1, Jovana Ilić Pajić2, Nataša Obradović3
1University of Belgrade, Innovation Centre of the Faculty of Technology and Metallurgy (e-mail: mvolic@tmf.bg.ac.rs), 2Institute of Chemistry, Technology and Metallurgy, National Institute of the Republic of Serbia, 3University of Belgrade, Faculty of Technology and Metallurgy
Orange peel is an abundant agro-industrial by-product rich in valuable essential oil, particularly D-limonene, but its full chemical and biological potential is often underutilized. Supercritical CO₂ extraction offers a sustainable, solvent-free approach for selective recovery of thermolabile terpenes, while Raman spectroscopy provides a rapid and non-destructive tool for extract characterization and quality control.
Introduction & Aim
Experimental
Conclusions
Results and discussion
Acknowledgement
000
The CO₂-extracted orange peel oil was dominated by D-limonene (92.7–96.7%), followed by β-pinene (1.20–1.69%), α-pinene (0.11–0.35%), sabinene (0.07–0.16%), and valencene (0.18–0.57%).
Raman spectroscopy confirmed the dominance of D-limonene and revealed process-dependent variations in the terpene composition.
This work was supported by the Ministry of Science, Technological Development and Innovation of the Republic of Serbia and Western Balkans Innovation Voucher Programme.
Supercritical CO₂ extraction enabled solvent-free recovery of essential oil from orange peel waste. Extraction conditions strongly affected both the yield and chemical profile of the obtained extracts. Raman spectroscopy demonstrated its potential for rapid, non-destructive quality control and process optimization.
Raw material
orange peel agro-industrial waste
drying: 40 °C, 24 h
moisture: 1.21%
particle size: ~0.20 mm
SFE conditions
Pressure: 10 / 12 / 14 MPa
Temperature: 40 / 45 / 50 °C
Extraction time: 1 h
CO₂ consumption: ~700 g
10MPOa
10 MPa / 40 °C
12 MPa / 40 °C
12 MPa / 50 °C