## Slide 1
28th Congress of SCTM, 23-26 September, Ohrid, Macedonia
ORANGE PEEL ESSENTIAL OIL AS A NATURAL SOLVENT FOR PROPOLIS: DEVELOPMENT AND CHARACTERIZATION OF AN OIL-BASED FORMULATION
Nataša Obradović1, Jovana Ilić Pajić2, Mina Volić Ollier3
1University of Belgrade, Faculty of Technology and Metallurgy (e-mail: ntomovic@tmf.bg.ac.rs), 2Institute of Chemistry, Technology and Metallurgy, National Institute of the Republic of Serbia, 3University of Belgrade, Innovation Centre of the Faculty of Technology and Metallurgy
Propolis is a natural source of bioactive compounds, but its conventional formulations are predominantly based on ethanol or other synthetic solvents, which limits their application in certain food and pharmaceutical products. This study aimed to develop and characterize a natural, alcohol-free oil formulation of propolis using orange peel essential oil as a functional terpene-rich solvent.
Introduction & Aim
Experimental
Conclusions
Results and discussion
Acknowledgement
BFT-P3
ORANGE PEEL
Agro-industrial by-product
HYDRODISTILLATION
Essential oil
GC–MS, HPLC
Chemical characterization
PROPOLIS
Dissolution in orange peel oil
Orange peel, an agro-industrial by-product, was subjected to hydrodistillation to obtain essential oil, which was subsequently characterized.
The obtained orange peel oil was dominated by D-limonene (97.09%), accompanied by smaller amounts of β-pinene (1.69%), α-pinene (0.45%), sabinene (0.43%), and valencene (0.08%).
TGA analysis
Selective antimicrobial activity of the formulations against Staphylococcus aureus and Candida albicans.
This work was supported by the Ministry of Science, Technological Development and Innovation of the Republic of Serbia and the Western Balkans Innovation Voucher Programme.
The developed formulation offers a natural, alcohol-free way to incorporate propolis bioactive compounds into an oil-based system while valorising orange peel agro-industrial waste.