## Slide 1
28th Congress of SCTM, 23-26 September, Ohrid, Macedonia
PCR-HRM Discrimination of Gluten-Containing and Gluten-Free Cereals
Mihaela Nedelkovska, Teona Spaseska, Marinela Cvetanoska, Pece Sherovski
Institute of Chemistry, Faculty of Natural Sciences and Mathematics, Ss. Cyril and Methodius University in Skopje,
Skopje, North Macedonia
The growing demand for gluten-free foods highlights the need for reliable methods to ensure their safety and authenticity, as accidental cross-contamination with gluten-containing cereals can occur during food production and distribution. This study aimed to develop and evaluate PCR-HRM (Polymerase Chain Reaction-High Resolution Melting) primers targeting the internal transcribed spacer (ITS) region for the discrimination of gluten-containing and gluten-free cereals.
Introduction & Aim
Experimental
OBPC-P7
Acknowledgement
This work was supported by the University Students' Assembly of the Ss. Cyril and Methodius University in Skopje through the project "Gluten detection using PCR methods: A new approach for monitoring commercial food products“.
Careful primer selection in the ITS region enables specific PCR-HRM differentiation between gluten-containing and gluten-free cereals.
Future optimization will test broader reference materials and food matrices to establish sensitivity and detection limits.
Conclusions
Target selection and primer design
Sample preparation
PCR Amplification & High-Resolution Melting (HRM)
Data analysis
Primer evaluation

## Slide 2
Results and discussion
P3 demonstrated high specificity, with clear discrimination between gluten-containing and gluten-free cereal samples.
P1 showed poor discrimination, with amplification detected across both target and
non-target cereals.
P2 improved discrimination but showed interference from oats.
DNA ladder
barley
wheat
rye
triticale
rice
corn
oats
Primer performance was assessed using Ct values, amplification and melting curves, and gel electrophoresis.
700 bp
500 bp
400 bp
300 bp
200 bp
150 bp
100 bp
75 bp
50 bp
25 bp
Gluten free
77.9 – 81.6 oC
Gluten containing
87.8 – 89.1 oC